## Slide 2: What can I do with a Raspberry Pi
By: Mike Linnen @mlinnen www.protosystem.net mlinnen@protosystem.net

## Slide 3: Agenda
What is a Raspberry Pi
Fun Projects
Internet of Things
First time setup
Notes: Answer the question What can I do with a Raspberry Pi?
More importantly is what can’t you do with a Raspberry Pi

## Slide 4: Got Kids?
FIRST Robotics Competition (FRC)
  Non-Profit Co. sponsoring robotic competitions to teach kids about engineering
  2,727 teams/robots
  68k high school students
  54 regional events, 4 qualifying champ, and 40 district events
  Software manages robotics competition (scheduling, ranking, lights , automated real-time scoring, monitoring robots)
  http://www.USFIRST.org

## Slide 5: What is a Raspberry Pi
Credit card sized single board computer
Teach computer science in schools at an affordable price
  Grade School, Middle School & High School
Design and Development started in 2006
Raspberry PI Foundation founded in 2009
Release to Market Feb 2012
3 Million sold by June 2014
Notes: In 2.25 years 3 million sold

## Slide 6: Hardware
Raspberry PI Model A $25 – 256 MB Ram, 1 USB, No Ethernet, GPIO 26
Raspberry PI Model B $35 – 512 MB Ram, 2 USB, Ethernet , GPIO 26
Raspberry PI Model B+ $35 - 512 MB Ram, 4 USB, Ethernet, GPIO 40
All have HDMI Out with Audio
All have Audio Jack out

## Slide 7: Components
Ethernet
Micro USB Power
USB 2.0
HDMI
RCA Video
Audio
GPIO
Camera Connector
Status LEDs
Notes: Pass around the broken Pi

## Slide 8: Operating Systems/Emulators
New out of the Box Software (NOOBS)
Raspian (Debian)
Pidora (Fedora)
Archlinux
Risc OS
RaspBMC
Openelec
Emulators
MS-DOS
ZX Spectrum
Commodore 64
Other Linux Based Distributions
Robot Operating System (ROS)
Android
Notes: Most popular Raspbian
ROS is a lot like Microsoft Robotics Studio (Service Oriented)

## Slide 9: Wall Mounted Google Calendar
http://tinyurl.com/PiLiveCalendar
Notes: Not touch friendly
Virtual Keyboard
Add appointments on you phone or tablet and they show up on the wall

## Slide 10: 64 Node Supercomputer
http://tinyurl.com/SuperComputerPi
Notes: University of Southhampton in UK
64 Raspberry Pi’s
Legos to hold them together
Low power/Portable
Hadoop
MPI - Message Passing Interface

## Slide 11: Christmas Light Show
http://tinyurl.com/PiLightShow
http://tinyurl.com/PiLightShowVideo
Notes: Raspberry Pi synchronized Christmas Light show using midi
Timidity is a midi synthesizer
Video
https://www.youtube.com/watch?v=Fb8107XZ8oI#t=12

## Slide 12: Arcade - MAME Gaming Console
MAME – Multiple Arcade Machine Emulator
Uses images of the original arcade ROMs

## Slide 13: DIY – Retro Gaming with Raspberry Pi
https://learn.adafruit.com/retro-gaming-with-raspberry-pi/overview

## Slide 14: Demo – MAME Gaming Console

## Slide 15: Programming the Raspberry Pi
Scratch – graphical programming environment
Python 2 or Python 3
C# using Mono
C/C++
Java
Javascript/Node
Perl
Go
……

## Slide 16: Python as a programming language
Python 2 or Python 3?
Object Oriented
Internet protocols (HTTP, FTP, SMTP, TCP/IP, POP, IMAP)
Unit Testing, Debugging and Profiling
Extensible via Modules or write you own c/c++ extensions

## Slide 17: Broken Build Notification
Continuous Integration Build
Raspberry Pi to Alert the team who broke the build
Python

## Slide 18: Broken Build Notification
Raspberry Pi

## Slide 19: Broken Build Notification
Visual Studio Online REST API
Raspberry Pi

## Slide 20: Broken Build Notification
Visual Studio Online REST API
Google Translate Text to Speech API
Raspberry Pi

## Slide 21: Broken Build Notification
Visual Studio Online REST API
Google Translate Text to Speech API
1
Requested By, Build Name
Raspberry Pi

## Slide 22: Broken Build Notification
Visual Studio Online REST API
Google Translate Text to Speech API
2
Text to Convert
Raspberry Pi

## Slide 23: Broken Build Notification
Visual Studio Online REST API
Google Translate Text to Speech API
3
MP3
Raspberry Pi

## Slide 24: DEMO: Broken Build Notification
Notes: protosystem.visualstudio.com
m_linnen@Hotmail.com login
introToRaspberyPi project
Show the code

## Slide 25: IoT – Internet of Things
Thing - Embedded Devices
Input - Sensors
Output - Actuators
Messaging - Machine 2 Machine communications
Cloud Services – Connector of Things
Gartner Forecasting 26 billion devices by 2020
Massive amounts of data

## Slide 26: Patterns for IoT Communications
Device (Thing) is a server that accepts inbound requests
Device (Thing) is a client that connects to a service
Device (Thing) is a client that connects to a broker

## Slide 27: Patterns for IoT Communications
Device (Thing) is a server that accepts inbound requests
  Easy to do by setting up a webserver on the device
  Ok for internal networks
  Need to open up ports on router/firewall
  Can be insecure
  Device can become overloaded with requests
  Tight coupling between the Device and whatever is communicating to it

## Slide 28: Patterns for IoT Communications
Device (Thing) is a client that connects to a service
  More secure than #1
  No need for ports to be opened up on router/firewall
  Device controls how fast it can process messages
  Device is still tightly couple to service

## Slide 29: Patterns for IoT Communications
Device (Thing) is a client that connects to a broker
  More secure then #1 (only outbound requests)
  No need for ports to be opened up on router/firewall
  Device controls how fast it can process messages
  You need a message broker between Thing and Service
  Decouples Thing from Service
  Publish/Subscribe model
  Multiple Subscribers
  Things can communicate to Things without a Service in between

## Slide 30: Broker Types
Local broker
  Not really IoT
  Ok for internal networks
Remote broker
  What if your internet access is down?
Local and Remote broker
  Higher reliability on internal network
  Allows for remote access when needed

## Slide 31: IoT Doorbell Ringer
3 Raspberry Pi’s distributed around the house
Doorbell pushed causes MP3 to be played on all 3 Pi’s
Connected Via MQTT message bus using a Remote Broker

## Slide 32: Demo: IoT Doorbell Ringer
MQTT Remote Broker
Pub/Sub
Front
Back
Upstairs
Raspberry Pi
Raspberry Pi
Raspberry Pi
Notes: 3 Pi’s connected via an MQTT Broker located in a cloud service
Cloud is not doing anything interesting except connecting the devices
Client02
Cd doorbell/mqtt/python
Sudo python pub_ring.py
Client01
Sudo python sub_ring.py
MediaServer
Sudo python sub_ring.py

## Slide 33: Code: pub_ring.py

## Slide 34: Code: sub_ring.py

## Slide 35: Node-RED (nodered.org)
Notes: MediaServer
LED + on pin 11
LED – on pin 6 GND
Cd node-red
sudo node red.js
http://mediaserver:1880
Use left & right mouse click to get the properties dialog open
Create an MQTT input with
test.mosquitto.org 1883
protosystemdemo/doorbell/ring
Create a switch on payload with 2 outputs 1=out 1 2 = out 2
Create a 3 sec trigger on out 1 – goes high then 3 secs later go low
Create a 6 sec trigger on out 2 – goes high then 6 secs later go low
Create a rpi-gpio output GPIO pin 11

## Slide 36: How would you enhance this doorbell?
When no-one is home play a barking dog along with the doorbell
Add a camera to take a snapshot of the person at the door
When it is after midnight ignore all doorbell ringing
If it is dark outside turn on a an outside light
Add a microphone to each Pi and use them as an intercom
Send text messages when the doorbell rings
Add other sensors like temperature, light, and motion.

## Slide 37: Media System - XBMC
Music
Movie
Stream
Pictures
PVR
Raspberry PI cheap Media System
  NOOBs has OpenELEC and RaspBMC

## Slide 38: Demo: Raspberry Pi & XBMC
MySQL
Movie & Music DBs
SMB Shares
Raspberry Pi
Raspberry Pi
Notes: Show shares on either Pi
All content on SMB shares
MySQL on Laptop
AdvancedSettings.xml

## Slide 39: Multi-Room Audio - Sonos

## Slide 40: DEMO: Multi-Room Audio Raspberry Pi
Logitech
Media Server
Raspberry PI (A)
Squeezelite Player
Family Room
Raspberry PI (A)
Squeezelite Player Deck
Raspberry PI (B)
Squeezelite Player Bonus
Raspberry PI (C)
Notes: http://mediaserver:9000 for the media server webpage
sudo service logitechmediaserver restart – to restart the service after boot up cause internet radio doesn’t work on first time boot
Start Squeeze Box Lite client on the Media Server device
/usr/bin/squeezelite-armv6hf -n FamilyRoom -m 00:04:20:00:00:01
Start Squeeze Box Lite client on the Client02 device
/usr/bin/squeezelite-armv6hf -n Deck
sudo alsamixer – to change the audio volume and device
Demo
Show two players exist
Play local music on 1st player
Play local music on 2nd player
Synchronize the players
Play streaming music on both players

## Slide 41: DEMO – Setup a new Squeezelite client
Notes: sudo alsamixer sets up the audio mixer and adjusts the sound level
mkdir squeezelite cd squeezelite
wget http://squeezelite-downloads.googlecode.com/git/squeezelite-armv6hf
sudo mv squeezelite-armv6hf /usr/bin
cd /usr/bin
sudo chmod a+x squeezelite-armv6hf
/usr/bin/squeezelite-armv6hf -n Bonus

## Slide 42: First time setup (what do you need?)
USB Keyboard
USB Mouse (only needed for the windowing environment)
Compatible SD Card (Class 4 or better 8 GB)
SD Card Reader
  Unless you got a pre-loaded SD Card
HDMI, HDMI to VGA or HDMI to DVI Cable
Monitor/TV that accepts an HDMI, DVI or VGA Cable input
Ethernet Cable

## Slide 43: First time setup (tips)
Use NOOBS to get started
  When formatting SD card don’t select your external USB drive by mistake
  Install multiple OS Distros to the same SD Card
    8 GB card can hold 3 OS’s
    16 GB card can hold all OS’s
  Set keyboard to US (default is British)
  Set Time Zone
  Set the HostName
  Install SAMBA for joining to Windows networks
  Clone SD Card when setup is complete as a backup

## Slide 44: DEMO - First Time Setup
Notes: pi/ and pword
sudo – super user Do, elevates privileges
sudo raspi-config
Change User Password
Change Timezone
Change keyboard layout -> Generic 104-key PC
Change hostname -> Advanced Options -> Host Name -> Demo
Verify ping/PuTTY and Windows explorer cannot see the Raspberry Pi
apt-get update – resynchronize the package index files from their sources
apt-get –u upgrade – shows what can be installed
apt-get upgrade – installs the newest versions of all packages currently installed
sudo apt-get update/upgrade
sudo apt-get install samba
sudo apt-get install samba-common-bin
Use PuTTY to remote into Pi to edit file
nano – a simple text file editor
sudo nano /etc/samba/smb.conf
change workgroup & wins support
add [pihome] section
sudo smbpasswd –a pi
sudo service samba restart
Test ping/PuTTY and Windows Explorer
sudo apt-get install xrdp
Demo x-windows

## Slide 45: DEMO - Good to know commands
Notes: man sudo manual for a comand
chmod – sets rights to a file or folder
ls/cd/mkdir/rmdir – basic file/directory manipulation
Command completion
apt-get remove –y wolfram-engine – removes installed packages
sudo shutdown –h now
wiringpi
gpio mode 14 down (pin 23)
gpio mode 10 down (pin 24)
gpio readall

## Slide 46: Tools nice to have
SD Formatter – prepare the card for an OS
Win32 Disk Imager – backup/restore SD card images
Router – DHCP Table shows Raspberry Pi’s IP address
PuTTY – windows remote ssh
VNC or xrpd – remoting into linux windowing environments

## Slide 47: Raspberry Pi vs Netduino/Arduino
 | Raspberry PI B (B+) | Netduino Plus 2 | Arduino Uno
Type | Mini-computer | Microcontroller | Microcontroller
OS | Linux | None | None
CPU | 32 bit 700 mhz | 32 bit 168 mhz | 8 bit 16 mhz
RAM | 256 mb | 100+ kb | 2 kb
GPIO | 8-21 (26) | 22 | 14
Other | 1-PWM, SPI, I2C, 1 UART (2- PWM) | 4-PWM, SPI, I2C, 1 UART, 6-AI | 6-PWM, SPI, I2C, 1 UART, 6-AI
Programming | Python, C/C++, JAVA, C# … | C#, VB.Net | C like
Ethernet | Onboard | Onboard | Add-on
Video | HDMI/RCA | None | None
Audio | Stereo Out, USB Mic | None | None
USB | 2 (4) | 1 | 0
Cost | $42 - $37 Pi & $5 SD Card | $59.95 | $24.99
Notes: At first glance Pi cost looks lot less
Netduino/Arduino for low level work
Raspberry Pi is field updatable

## Slide 48: Accessories – Wifi USB
$5
Great for areas that don’t have Cat-5

## Slide 49: Accessories – PI Face
Expansion Board sits on top of the PI
2 Relays
8 Outputs
8 Inputs
8 LED
4 Switches
$35
Great for prototyping

## Slide 50: Accessories - Camera
Connects to PI via special port
5 mp Camera
1080p 30 fps
$28

## Slide 51: Accessories – HDMI to VGA
Hook up Raspberry PI to a non-HDMI monitor
$8

## Slide 52: Accessories – Breakout board
Easily hook up PI to breadboard
$9